## Slide 1: Electrical Power & Energy
James
Watt
James
Prescott
Joule

## Slide 2
Power (P):
A measure of the rate of transfer of energy.
James Watt
Power is measured in
watts
( W )
P = V I
Power
Potential
Difference
Current
( W )
( V )
( A )

## Slide 3
Example I:
What current will be drawn by an 85 W Fender Twin Reverb amplifier if it is connected to a 120 V outlet?
P = V I
85
=
120
I
I
=
120
120
0.71
A
P = 85 W
V = 120 V
I = ?

## Slide 4
Example II:
How much power will be dissipated by a 20 W resistor that is connected to a potential difference of 6 V?
R = 20 W
V = 6 V
P = ?
André Ampère
Georg Ohm
Use my formula
We need to know the current to find the power
P = V I

## Slide 5
Example II:
How much power will be dissipated by a 20 W resistor that is connected to a potential difference of 6 V?
R = 85 W
V = 6 V
P = ?
V = R I
Georg Ohm
Use my formula
André Ampère
We need to know the current to find the power
P = V I

## Slide 6
Example II:
How much power will be dissipated by a 20 W resistor that is connected to a potential difference of 6 V?
P = V I
6
=
20
I
I
=
20
20
0.3
A
R = 20 W
V = 6 V
P = ?
V = R I
P =
( 6 )
( 0.3 )
P =
1.8
W

## Slide 7
Energy (E):
A measure of the ability to do work.
James Prescott Joule
Energy is usually measured in
joules
( J )
E = P t
Energy
Power
time
( J )
( W )
( s )

## Slide 8
Example III:
How much energy (in joules) is used by a 2 kW heater if it is operated at full power for 12 minutes?
E = P t
E =
( 2000 )
1 440 000
J
P = 2 kW
t = 12 min
E = ?
= ______ W
2000
= ______ s
720
E =
( 720 )

## Slide 9
Unfortunately, energy is not just measured in joules.
E = P t
( kWh )
( kW )
( h )
When measuring electrical energy consumption for an electricity bill,
energy is measured in kilowatt-hours ( kWh )
Uh, oh …

## Slide 10
Example IV:
How much energy (in kilowatt-hours) is used by a 2 kW heater if it is operated at full power for 12 minutes?
E = P t
E =
( 2 )
0.4
kWh
P = 2 kW
t = 12 min
E = ?
= ______ h
0.2
E =
( 0.2 )

## Slide 11
Oh, no …
E = P t
Energy can even be measured in watt-hours ( Wh )
And that’s not all …
( Wh )
( W )
( h )