## Slide 1
Resistance
Current
Voltage
V vs I

## Slide 2
Slope = R
I
V
Slope = a
x
y
Math Class
Electricity
y =
V =
a x
R I

## Slide 3
Mathematical relation between Voltage, Resistance and Current
V
R
I
Alessandro Volta
Georg Ohm
André-Marie Ampère
=
Ohm’s Law
in Volts (V)
in Amps ()
in Ohms ()

## Slide 4
V = R I
Example I:
What current will travel through a component that has a resistance of 60 W if it is connected to a 12 V battery?
12
=
60
I
I
=
60
60
0.2
A
R = 60 W
V = 12 V
I = ?

## Slide 5
Example II:
What reading should appear on the voltmeter in the circuit below?
V
A
20 W

## Slide 6
Example II:
What reading should appear on the voltmeter in the circuit below?
V
A
I = 70 mA
20 W

## Slide 7
V = R I
Example II:
What reading should appear on the voltmeter in the circuit below?
V =
( 20 )
( 0.07 )
V
A
I = 70 mA
20 W
V =
1.4
V
R = 20 W
V = ?
I = 70 mA
= ______ A
0.07

## Slide 8
Example III:
The human body has an electrical resistance of about 10 kW. (it actually can vary from 1 kW – 100 kW)
Refer to the given chart to determine the (usual) effect of touching an uninsulated wire from a 120 V outlet.
I (mA) | Effect on a person
0.5 - 3 | Tingling sensations
3 - 10 | Muscle contractions and pain
10 - 40 | ‘Let-go’ threshold
30 - 75 | Respiratory paralysis
100 - 200 | Ventricular fibrillation (Death)
200 - 500 | Heart clamps tight
1500+ | Tissues and organs burn

## Slide 9
Example III:
The human body has an electrical resistance of about 10 kW. (it actually can vary from 1 kW – 100 kW)
Refer to the given chart to determine the (usual) effect of touching an uninsulated wire from a 120 V outlet.
I = ?
V = 120 V
R = 10 kW
= _______ W
10 000
I (mA) | Effect on a person
0.5 - 3 | Tingling sensations
3 - 10 | Muscle contractions and pain
10 - 40 | ‘Let-go’ threshold
30 - 75 | Respiratory paralysis
100 - 200 | Ventricular fibrillation (Death)
200 - 500 | Heart clamps tight
1500+ | Tissues and organs burn
V = R I
120 =
10 000
I
I =
0.012
A
10 000
10 000
I =
12
mA